#### 0907231 Digital Logic (Fall 2008)

#### Quiz 1B

الاسم:					رقم التسجيل:	 		رقم الشعبة:

===========================================================================

Instructions: Time 10 minutes. Closed books and notes. No calculators. No questions are allowed.

Q. Convert the following number from the given base to the other three bases listed in the table:

| Decimal | Binary | Octal | Hexadecimal |
| --- | --- | --- | --- |
| 671.25 | 1010011111.01 | 1237.2 | 29F.2 |

1237.2 to Binary is 001 010 011 111 . 010

To Hex		2	9	F	.	2

Octal to Decimal 	1*8*8*8 + 2*8*8 + 3*8 + 7*1 + 2/8 = 512 + 128 + 24 + 7 + .25

= 671.25

(One mark for each answer)

Q. Prove the identity of the following Boolean equation, using algebraic manipulation (Y’ is NOT Y).

X · (X · Y)’ = XY’

X · (X · Y)’		= X ( (X’ + Y’)

= XX’ + XY’

= 0 + XY’

= XY’

(Three makrs)

<Good Luck>