Homework 1

Problem 1

Convert the following numbers from the given base to the other three bases listed in the table:

| Decimal | Binary | Octal | Hexadecimal |
| --- | --- | --- | --- |
| 144.75 | ? | ? | ? |
| ? | 10110101.101 | ? | ? |
| ? | ? | 451.3 | ? |
| ? | ? | ? | F39B.C |

Problem 2

Perform the following binary operations:

| a) 0101 + 0011 | b) 0101 + 1011 | c) 100111 + 011011 |
| --- | --- | --- |
| d) 0101 - 0011 | e) 1011 - 0101 | f) 100111 - 011011 |
| g) 0101 * 0011 | h) 1011 * 0101 | i) 100111 * 011011 |

Problem 3

Represent the decimal numbers 694 and 835 in BCD, and show the steps necessary to find their sum.

Problem 4

List the 6-bit binary numbers equivalent to the decimal numbers 27 through 35. Also add a parity bit in the rightmost position giving even parity to the overall 7-bit binary string.

| Decimal Number | Parity | Binary Number |
| --- | --- | --- |
| 26 | 1 | 011010 |
| 27 |  |  |
| 28 |  |  |
| 29 |  |  |
| 30 |  |  |
| 31 |  |  |
| 32 |  |  |
| 33 |  |  |
| 34 |  |  |
| 35 |  |  |

Problem 5

What are the ASCII codes (in binary, hexadecimal, and decimal) of the following characters?

- ‘ ’ (space)

- ‘+’

- ‘0’

- ‘1’

- ‘C’

- ‘D’

- ‘c’

- ‘d’

Problem 6

Demonstrate by means of truth tables the validity of the following identity:

X + YZ = (X + Y)(X+ Z)

Problem 7

Prove the identity of each of the following Boolean equations, using algebraic manipulation.

- Y + X’Z + XY’ = X + Y + Z

- ABC’ + BC’D’ + BC + C’D = B + C’D