## Slide 1
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Introduction
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits “Instruction Level Parallelism”
Beyond this, there are two main approaches:
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMP processors
  Compiler-based static approaches
    Not as successful outside of scientific applications
Introduction

## Slide 3: Instruction-Level Parallelism
When exploiting instruction-level parallelism, goal is to maximize CPI
  Pipeline CPI =
    Ideal pipeline CPI +
    Structural stalls +
    Data hazard stalls +
    Control stalls
Parallelism with basic block is limited
  Typical size of basic block = 3-6 instructions
  Must optimize across branches
Introduction

## Slide 4: Data Dependence
Loop-Level Parallelism
  Unroll loop statically or dynamically
  Use SIMD (vector processors and GPUs)
Challenges:
  Data dependency
    Instruction j is data dependent on instruction i if
      Instruction i produces a result that may be used by instruction j
      Instruction j is data dependent on instruction k and instruction k is data dependent on instruction i
Dependent instructions cannot be executed simultaneously
Introduction

## Slide 5: Data Dependence
Dependencies are a property of programs
Pipeline organization determines if dependence is detected and if it causes a stall
Data dependence conveys:
  Possibility of a hazard
  Order in which results must be calculated
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect
Introduction

## Slide 6: Name Dependence
Two instructions use the same name but no flow of information
  Not a true data dependence, but is a problem when reordering instructions
  Antidependence: instruction j writes a register or memory location that instruction i reads
    Initial ordering (i before j) must be preserved
  Output dependence: instruction i and instruction j write the same register or memory location
    Ordering must be preserved
To resolve, use renaming techniques
Introduction

## Slide 7: Other Factors
Data Hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)
Control Dependence
  Ordering of instruction i with respect to a branch instruction
    Instruction control dependent on a branch cannot be moved before the branch so that its execution is no longer controller by the branch
    An instruction not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
Introduction

## Slide 8: Examples
OR instruction dependent on DADDU and DSUBU
Assume R4 isn’t used after skip
  Possible to move DSUBU before the branch
Introduction
Example 1:
DADDU R1,R2,R3
BEQZ R4,L
DSUBU R1,R1,R6
L: …
OR R7,R1,R8
Example 2:
DADDU R1,R2,R3
BEQZ R12,skip
DSUBU R4,R5,R6
DADDU R5,R4,R9
skip:
OR R7,R8,R9

## Slide 9: Compiler Techniques for Exposing ILP
Pipeline scheduling
  Separate dependent instruction from the source instruction by the pipeline latency of the source instruction
Example:
  for (i=999; i>=0; i=i-1)
  x[i] = x[i] + s;
Compiler Techniques

## Slide 10: Pipeline Stalls
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (assume integer load latency is 1)
BNE R1,R2,Loop
Compiler Techniques

## Slide 11: Pipeline Scheduling
Scheduled code:
Loop: L.D F0,0(R1)
DADDUI R1,R1,#-8
ADD.D F4,F0,F2
stall
stall
S.D F4,8(R1)
BNE R1,R2,Loop
Compiler Techniques

## Slide 12: Loop Unrolling
Loop unrolling
  Unroll by a factor of 4 (assume # elements is divisible by 4)
  Eliminate unnecessary instructions
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D F4,0(R1) ;drop DADDUI & BNE
L.D F6,-8(R1)
ADD.D F8,F6,F2
S.D F8,-8(R1) ;drop DADDUI & BNE
L.D F10,-16(R1)
ADD.D F12,F10,F2
S.D F12,-16(R1) ;drop DADDUI & BNE
L.D F14,-24(R1)
ADD.D F16,F14,F2
S.D F16,-24(R1)
DADDUI R1,R1,#-32
BNE R1,R2,Loop
Compiler Techniques
note: number of live registers vs. original loop

## Slide 13: Loop Unrolling/Pipeline Scheduling
Pipeline schedule the unrolled loop:
Loop: L.D F0,0(R1)
L.D F6,-8(R1)
L.D F10,-16(R1)
L.D F14,-24(R1)
ADD.D F4,F0,F2
ADD.D F8,F6,F2
ADD.D F12,F10,F2
ADD.D F16,F14,F2
S.D F4,0(R1)
S.D F8,-8(R1)
DADDUI R1,R1,#-32
S.D F12,16(R1)
S.D F16,8(R1)
BNE R1,R2,Loop
Compiler Techniques

## Slide 14: Strip Mining
Unknown number of loop iterations?
  Number of iterations = n
  Goal: make k copies of the loop body
  Generate pair of loops:
    First executes n mod k times
    Second executes n / k times
    “Strip mining”
Compiler Techniques

## Slide 15: Branch Prediction
Basic 2-bit predictor:
  For each branch:
    Predict taken or not taken
    If the prediction is wrong two consecutive times, change prediction
Correlating predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding n branches
Local predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes for the last n occurrences of this branch
Tournament predictor:
  Combine correlating predictor with local predictor
Branch Prediction

## Slide 16: Branch Prediction Performance
Branch Prediction
Branch predictor performance

## Slide 17: Dynamic Scheduling
Rearrange order of instructions to reduce stalls while maintaining data flow
Advantages:
  Compiler doesn’t need to have knowledge of microarchitecture
  Handles cases where dependencies are unknown at compile time
Disadvantage:
  Substantial increase in hardware complexity
  Complicates exceptions
Branch Prediction

## Slide 18: Dynamic Scheduling
Dynamic scheduling implies:
  Out-of-order execution
  Out-of-order completion
Creates the possibility for WAR and WAW hazards
Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards
Branch Prediction

## Slide 19: Register Renaming
Example:
DIV.D F0,F2,F4
ADD.D F6,F0,F8
S.D F6,0(R1)
SUB.D F8,F10,F14
MUL.D F6,F10,F8
+ name dependence with F6
Branch Prediction
antidependence
antidependence

## Slide 20: Register Renaming
Example:
DIV.D F0,F2,F4
ADD.D S,F0,F8
S.D S,0(R1)
SUB.D T,F10,F14
MUL.D F6,F10,T
Now only RAW hazards remain, which can be strictly ordered
Branch Prediction

## Slide 21: Register Renaming
Register renaming is provided by reservation stations (RS)
  Contains:
    The instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
  RS fetches and buffers an operand as soon as it becomes available (not necessarily involving register file)
  Pending instructions designate the RS to which they will send their output
    Result values broadcast on a result bus, called the common data bus (CDB)
  Only the last output updates the register file
  As instructions are issued, the register specifiers are renamed with the reservation station
  May be more reservation stations than registers
Branch Prediction

## Slide 22: Tomasulo’s Algorithm
Load and store buffers
  Contain data and addresses, act like reservation stations
Top-level design:
Branch Prediction

## Slide 23: Tomasulo’s Algorithm
Three Steps:
  Issue
    Get next instruction from FIFO queue
    If available RS, issue the instruction to the RS with operand values if available
    If operand values not available, stall the instruction
  Execute
    When operand becomes available, store it in any reservation stations waiting for it
    When all operands are ready, issue the instruction
    Loads and store maintained in program order through effective address
    No instruction allowed to initiate execution until all branches that proceed it in program order have completed
  Write result
    Write result on CDB into reservation stations and store buffers
      (Stores must wait until address and value are received)
Branch Prediction

## Slide 24: Example
Branch Prediction

## Slide 25: Hardware-Based Speculation
Execute instructions along predicted execution paths but only commit the results if prediction was correct
Instruction commit: allowing an instruction to update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits
  I.e. updating state or taking an execution
Branch Prediction

## Slide 26: Reorder Buffer
Reorder buffer – holds the result of instruction between completion and commit
Four fields:
  Instruction type: branch/store/register
  Destination field: register number
  Value field: output value
  Ready field: completed execution?
Modify reservation stations:
  Operand source is now reorder buffer instead of functional unit
Branch Prediction

## Slide 27: Reorder Buffer
Register values and memory values are not written until an instruction commits
On misprediction:
  Speculated entries in ROB are cleared
Exceptions:
  Not recognized until it is ready to commit
Branch Prediction

## Slide 28: Multiple Issue and Static Scheduling
To achieve CPI < 1, need to complete multiple instructions per clock
Solutions:
  Statically scheduled superscalar processors
  VLIW (very long instruction word) processors
  dynamically scheduled superscalar processors
Multiple Issue and Static Scheduling

## Slide 29: Multiple Issue
Multiple Issue and Static Scheduling

## Slide 30: VLIW Processors
Package multiple operations into one instruction
Example VLIW processor:
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Must be enough parallelism in code to fill the available slots
Multiple Issue and Static Scheduling

## Slide 31: VLIW Processors
Disadvantages:
  Statically finding parallelism
  Code size
  No hazard detection hardware
  Binary code compatibility
Multiple Issue and Static Scheduling

## Slide 32: Dynamic Scheduling, Multiple Issue, and Speculation
Modern microarchitectures:
  Dynamic scheduling + multiple issue + speculation
Two approaches:
  Assign reservation stations and update pipeline control table in half clock cycles
    Only supports 2 instructions/clock
  Design logic to handle any possible dependencies between the instructions
  Hybrid approaches
Issue logic can become bottleneck
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 33: Overview of Design
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 34: Multiple Issue
Limit the number of instructions of a given class that can be issued in a “bundle”
  I.e. on FP, one integer, one load, one store
Examine all the dependencies amoung the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Also need multiple completion/commit
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 35: Example
Loop: LD R2,0(R1) ;R2=array element
DADDIU R2,R2,#1 ;increment R2
SD R2,0(R1) ;store result
DADDIU R1,R1,#8 ;increment pointer
BNE R2,R3,LOOP ;branch if not last element
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 36: Example (No Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 37: Example
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 38: Branch-Target Buffer
Need high instruction bandwidth!
  Branch-Target buffers
    Next PC prediction buffer, indexed by current PC
Adv. Techniques for Instruction Delivery and Speculation

## Slide 39: Branch Folding
Optimization:
  Larger branch-target buffer
  Add target instruction into buffer to deal with longer decoding time required by larger buffer
  “Branch folding”
Adv. Techniques for Instruction Delivery and Speculation

## Slide 40: Return Address Predictor
Most unconditional branches come from function returns
The same procedure can be called from multiple sites
  Causes the buffer to potentially forget about the return address from previous calls
Create return address buffer organized as a stack
Adv. Techniques for Instruction Delivery and Speculation

## Slide 41: Integrated Instruction Fetch Unit
Design monolithic unit that performs:
  Branch prediction
  Instruction prefetch
    Fetch ahead
  Instruction memory access and buffering
    Deal with crossing cache lines
Adv. Techniques for Instruction Delivery and Speculation

## Slide 42: Register Renaming
Register renaming vs. reorder buffers
  Instead of virtual registers from reservation stations and reorder buffer, create a single register pool
    Contains visible registers and virtual registers
  Use hardware-based map to rename registers during issue
  WAW and WAR hazards are avoided
  Speculation recovery occurs by copying during commit
  Still need a ROB-like queue to update table in order
  Simplifies commit:
    Record that mapping between architectural register and physical register is no longer speculative
    Free up physical register used to hold older value
    In other words: SWAP physical registers on commit
  Physical register de-allocation is more difficult
Adv. Techniques for Instruction Delivery and Speculation

## Slide 43: Integrated Issue and Renaming
Combining instruction issue with register renaming:
  Issue logic pre-reserves enough physical registers for the bundle (fixed number?)
  Issue logic finds dependencies within bundle, maps registers as necessary
  Issue logic finds dependencies between current bundle and already in-flight bundles, maps registers as necessary
Adv. Techniques for Instruction Delivery and Speculation

## Slide 44: How Much?
How much to speculate
  Mis-speculation degrades performance and power relative to no speculation
    May cause additional misses (cache, TLB)
  Prevent speculative code from causing higher costing misses (e.g. L2)
Speculating through multiple branches
  Complicates speculation recovery
  No processor can resolve multiple branches per cycle
Adv. Techniques for Instruction Delivery and Speculation

## Slide 45: Energy Efficiency
Speculation and energy efficiency
  Note: speculation is only energy efficient when it significantly improves performance
Value prediction
  Uses:
    Loads that load from a constant pool
    Instruction that produces a value from a small set of values
  Not been incorporated into modern processors
  Similar idea--address aliasing prediction--is used on some processors
Adv. Techniques for Instruction Delivery and Speculation

## Slide 46: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 47: The ARM Cortex-A8
Used in iPhone 4
Dual-issue, statically scheduled, dynamic issue detection, 0-2 instructions issue/clock.
13-stage pipeline

## Slide 48: The ARM Cortex-A8

## Slide 49: The ARM Cortex-A8

## Slide 50: The Intel Core i7