## Slide 1: Appendix D: Multi-Cycle Datapath and Control
Dr. Iyad F. Jafar
Adapted from Dr. Gheith Abandah slides
http://www.abandah.com/gheith/Courses/CPE335_S08/index.html

## Slide 2: Outline
Introduction
Multi-cycle Datapath
Multi-cycle Control
Performance Evaluation

## Slide 3: Introduction
The single-cycle datapath is straightforward, but...
  Hardware duplication
    It has to use one ALU and two 32-bit adders
    It has separate Instruction and Data memories
  Cycle time is determined by worst-case path! Time is wasted for instructions that finish earlier!!
Can we do any better?
  Break the instruction execution into steps
  Each step finishes in one shorter cycle
  Since instructions differ in number of steps, so will the number of cycles! Thus, time is different!
  Multi-Cycle implementation!

## Slide 4: Multi-Cycle Datapath
Instruction execution is done over multiple steps such that
  Each step takes one cycle
  The amount of work done per cycle is balanced
  Restrict each cycle to use one major functional unit
Expected benefits
  Time to execute different instructions will be different (Better Performance!)
  The cycle time is smaller (faster clock rate!)
  Allows functional units to be used more than once per instruction as long as they are used in different cycles
    One memory is needed!
    One ALU is needed!

## Slide 5: Multi-Cycle Datapath
Requirements
  Keep in mind that we have one ALU, Memory, and PC
  Thus,
    Add/expand multiplexors at the inputs of major units that are used differently across instructions
    Add intermediate registers to hold values between cycles !!
    Define additional control signals and redesign the control unit

## Slide 6: Multi-Cycle Datapath
Requirements - ALU
  Operations
    Compute PC+4
    Compute the Branch Address
    Compare two registers
    Perform ALU operations
    Compute memory address
  Thus, the first ALU input could be
    R[rs] (R-type)
    PC (PC = PC + 4)
     Add a MUX and define the ALUScrA signal
  The second ALU input could be
    R[rt] (R-type)
    A constant value of 4 (to compute PC + 4)
    Sign-extended immediate (to compute address of LW and SW)
    Sign-extended immediate x 4 (compute branch address for BEQ)
    Expand the MUX at the second ALU input and make the ALUSrcB signal two bits
  The values read from register file will be used in the next cycle
   Add the A and B registers
  The ALU result (R-type result or memory address) will be used in the following cycle
     Add the ALUOut register

## Slide 7: Multi-Cycle Datapath
Requirements - PC
  PC input could be
    PC + 4 (sequential execution)
    Branch address
    Jump address
     The PCSrc signal
  The PC is not written on every cycle
    Define the PCWrite singal (for ALU, Jump, and Memory)
    The PCWriteCond singal (BEQ)

## Slide 8: Multi-Cycle Datapath
Requirements – Memory
  Memory input could be
      Memory address from PC
      Memory address from ALU
       Add MUX at the address port of the memory and define the IorD signal
  Memory output could be
    Instruction
    Data
    Add the IR register to hold the instruction
    Add the MDR register to hold the data loaded from memory (Load)
  The IR is not written on every cycle
    Define the IRWrite signal

## Slide 9: Multi-Cycle Datapath
Address
Read Data
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUOut
Sign
Extend
Shift
left 2
ALU
control
Shift
left 2
ALUOp
Control
IRWrite
MemtoReg
MemWrite
MemRead
IorD
PCWrite
PCWriteCond
RegDst
RegWrite
ALUSrcA
ALUSrcB
zero
PCSource
1
1
1
1
1
1
0
0
0
0
0
0
2
2
3
4
func
Address Field
PC[31-28]
Offset
opcode
32
28
rs
rt
rd
4
26
32
Notes: Why the branch instruction finish in three cycles? Why the branch address is taken from the ALUOut register not from the ALU output?
 The branch address is computed in the decode cycle and stored in the ALU register. In the next cycle, the ALU is used to compare the two registers, thus the output is not the branch address. However, at the end of the execute cycle, the branch address is already at the input of the PC and it will not be overwritten until the rising edge arrives.

## Slide 10: Multi-Cycle Control Signals
Signal Name | Effect when Deasserted (0) | Effect when Asserted (1)
RegDst | The destination register number comes from the rt field | The destination register number comes from the rd field
RegWrite | None | Write is enabled to selected destination register
ALUSrcA | The first ALU operand is the PC | The first ALU operand is register A
MemRead | None | Content of memory address is placed on Memory data out
MemWrtite | None | Memory location specified by the address is replaced by the value on Write data input
MemtoReg | The value fed to register file is from ALUOut | The value fed to register file is from memory
IorD | PC is used as an address to memory unit | ALUOut is used to supply the address to the memory unit
IRWrite | None | The output of memory is written into IR
PCWrite | None | PC is written; the source is controlled by PCSource
PCWriteCond | None | PC is written if Zero output from ALU is also active

## Slide 11: Multi-Cycle Control Signals
Signal | Value | Effect
ALUOp | 00 | ALU performs add operation
 | 01 | ALU performs subtract operation
 | 10 | The funct field of the instruction determines the ALU operation
ALUSrcB | 00 | The second input to the ALU comes from register B
 | 01 | The second input to the ALU is 4 (to increment PC)
 | 10 | The second input to the ALU is the sign extended offset , lower 16 bits of IR.
 | 11 | The second input to the ALU is the sign extended , lower 16 bits of the IR shifted left by two bits
PCSource | 00 | Output of ALU (PC +4) is sent to the PC for writing
 | 01 | The content of ALUOut are sent to the PC for writing (Branch address)
 | 10 | The jump address is sent to the PC for writing

## Slide 12: Instruction Execution
The execution of instructions is broken into multiple cycles
In each cycle, only one major unit is allowed to be used
The major units are
  The ALU
  The Memory
  The Register File
Keep in mind that not all instructions use all the major functional units
In general we may need up to five cycles
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Fetch
Decode
Execute
Memory
WB

## Slide 13: Instruction Execution
Cycle 1 – Fetch
  Same for all instructions
  Operations
    Send the PC to fetch instruction from memory and store in IR
IR  Mem[PC]
    Update the PC
PC  PC + 4
  Control Signals
    IorD = 0 (Select the PC as an address)
    MemRead = 1 (Reading from memory)
    IRWrite = 1 (Update PC)
    ALUSrcA = 0 (Select PC as first input to ALU)
    ALUSrcB = 01 (Select 4 as second input to ALU)
    ALUOp = 00 (Addition)
    PCWrite = 1 (Update PC)
    PCSrc = 00 (Select PC+4)

## Slide 14: Instruction Execution
Cycle 2 – Decode
  Operations
    Read two registers based on the rs and rt fields and store them in the A and B registers
A  Reg[IR[25:21] ]
B  Reg[IR[20:16]]
    Use the ALU to compute the branch address
ALUOut  PC + (sign-extend(IR[15:0]) <<2)
    Is it always a branch instruction???
  Control Signals
    ALUSrcA = 0 (Select PC+4)
    ALUSrcB = 11 (Select the sign-extended offsetx4)
    ALUOp = 00 (Add operation)

## Slide 15: Instruction Execution
Cycle 3 – Execute & Branch and Jump Completion
  The instruction is known!
  Different operations depending on the instruction
  Operations
    Memory Access Instructions (Load or Store)
      Use the ALU to compute the memory address
ALUOut  A + sign-extend(IR[15:0])
      Control Signals
        ALUSrcA = 1 (Select A register)
        ALUSrcB = 10 (Select the sign-extended offset)
        ALUOp = 00 (Addition operation)

## Slide 16: Instruction Execution
Cycle 3 – Execute & Branch and Jump Completion
  Operations
    ALU instructions
      Perform the ALU operation according to the ALUop and Func between registers A and B
ALUOut  A op B
      Control Signals
        ALUSrcA = 1 (Select A register)
        ALUSrcB = 00 (Select B register)
        ALUOp = 10 (ALUoperation)

## Slide 17: Instruction Execution
Cycle 3 – Execute & Branch and Jump Completion
  Operations
    Branch Equal Instruction
      Compare the two registers
if (A == B) then PC  ALUOut
      Control Signals
        ALUSrcA = 1 (Select A register)
        ALUSrcB = 00 (Select B register)
        ALUOp = 01 (Subtract)
        PCWriteCond = 1 (Branch instruction)
        PCSrc = 01 (Select branch address)

## Slide 18: Instruction Execution
Cycle 3 – Execute & Branch and Jump Completion
  Operations
    Jump Instruction
      Generate the jump address
PC  {PC[31:28], (IR[25:0],2’b00)}
      Control Signals
        PCSrc = 10 (Select jump address)
        PCWrite = 1 (Write the PC)
Notes: Why not to finish the jump instruction in the second cycle??!

## Slide 19: Instruction Execution
Cycle 4 – Memory Read or R-type and Store Completion
  Different operations depending on the instruction
  Operations
    Load instruction
      Use the computed address (found in ALUOut) , read from memory and store value in MDR
MDR  Memory[ALUOut]
      Control Signals
        IorD = 1 (Address is for data)
        MemRead = 1 (Read from memory)
    Store instruction
      Use the computed address to store the value in register B into memory
Memory[ALUOut]  B
      Control Signals
        IorD = 1 (Address is for data)
        MemWrite = 1 (Write to memory)

## Slide 20: Instruction Execution
Cycle 4 – Memory Read or R-type and Store Completion
  Operations
    ALU instructions
      Write the results (ALUOut) into the register filer
Reg[IR[15:11]]  ALUOut
      Control Signals
        MemToReg = 0 (Data is from ALUOut)
        RegDest = 1 (Destination is rd)
        RegWrite = 1 (Write to register)

## Slide 21: Instruction Execution
Cycle 5 – Memory Read Completion
  Needed for Load instructions only
  Operations
    ALU instructions
      Store the value loaded from memory and found in the MDR register in the register file based on the rt field of the instruction
  Reg[IR[20:16]]  MDR
      Control Signals
        MemToReg = 1 (Data is from MDR)
        RegDest = 0 (Destination is rt)
        RegWrite = 1 (Write to register)

## Slide 22: Instruction Execution
In the proposed multi-cycle implementation, we may need up to five cycles to execute the supported instructions
Instruction Class | Clock Cycles Required
Load | 5
Store | 4
Branch | 3
Arithmetic-logical | 4
Jump | 3

## Slide 23: Multi-Cycle Control
(1) FSM Implementation
The control of single-cycle is simple! All control signals are generated in the same cycle!
However, this is not true for the multi-cycle approach:
  The instruction execution is broken to multiple cycles
  Generating control signals is not determined by the opcode only! It depends on the current cycle as well!
  In order to determine what to do in the next cycle, we need to know what was done in the previous cycle!
  Memorize ! Finite state machine (Sequential circuit)!
Combinational
control logic
State Reg
Inst
Opcode
Datapath
control
points
Next State
. . .
. . .
. . .
FSM
A set of states (current state stored in State Register)
Next state function (determined by current state and the input)
Output function (determined by current state and the input)

## Slide 24: Multi-Cycle Control
Need to build the state diagram
  Add a state whenever different operations are to be performed
  For the supported instructions, we need 10 different states (next slide)
  The first two states are the same for all instructions
Once the state diagram is obtained, build the state table, derive combinational logic responsible for computing next state and outputs

## Slide 25
(0) Fetch
START
(1) Decode
ALUSrcA = 0
ALUSrcB = 11
ALUOp = 00
MemRead = 1
ALUSrcA = 0
IorD = 0
IRWrite = 1
ALUSrcB = 01
ALUOp = 00
PCWrite = 1
PCSrc = 00
PCWrite = 1
PCSrc = 10
ALUSrcA = 1
ALUSrcB = 00
ALUOp = 01
PCWriteCond = 1
PCSrc = 01
ALUSrcA = 1
ALUSrcB = 00
ALUOp = 10
RegDst = 1
RegWrite = 1
MemtoReg = 0
Op = J
Op = BEQ
Op = R-type
Op = LW
Op = SW
ALUSrcA = 1
ALUSrcB = 10
ALUOp = 00
MemWrite = 1
IorD = 1
Op = SW
MemRead = 1
IorD = 1
RegDst = 0
RegWrite = 1
MemtoReg = 1
Op = LW
(9) Branch
Completion
(8) Jump
Completion
(7) R-Type
Completion
(5) SW
Completion
(4) LW
Completion
(2) Memory
Address
Computation
(6) Execute
Multi-cycle
State
Diagram
(3) Memory Access

## Slide 26: Multi-Cycle Control
(2) ROM Implementation
  FSM design
    10 inputs
    20 outputs
    TT size = 210x20
  ROM
    Can be used to implement the truth table above
    Each location stores the control signals values and the next state
    Each location is addressable by the opcode and next state value
210x20
ROM
Control Logic
Data
Address
State Register
Opcode
PCWrite
PCWriteCond
IorD
MemRead
MemWrite
IRWrite
MemToReg
PCSrc
ALUOp
ALUSrcB
ALUSrcA
RegWrite
RegDst
Op5
Op4
Op3
Op2
Op1
Op0
S3
S2
S1
S0
NS0
NS1
NS2
NS3

## Slide 27: Multi-Cycle Control
(3) Microprogramming
ROM implementation is vulnerable to bugs and expensive especially for complex CPU.
Size increase as the number and complexity of instructions (states) increases
Use Microprogramming
  Some sort of a programming language!
  The next state might not be sequential
  Generate the next state outside the ROM
  Each state is a micro instruction and the signals are specified symbolically
  Use labels for sequencing

## Slide 28: Multi-Cycle Control
(3) Microprogramming
10x17
ROM
Control Logic
Data
Address
PCWrite
PCWriteCond
IorD
MemRead
MemWrite
IRWrite
MemToReg
PCSrc
ALUOp
ALUSrcB
ALUSrcA
RegWrite
RegDst
State
Address Select Logic
1
Opcode
AddCtrl

## Slide 29: Multi-Cycle Control
(3) Microprogramming
Inside the address select logic
State
1
Opcode
AddCtrl
Dispatch ROM 2
Dispatch ROM 1
MUX
3 2 1 0
0
To ROM

## Slide 30: Multi-Cycle Control
(3) Microprogramming
Inside the address select logic

## Slide 31: Multi-Cycle Control
(3) Microprogramming
Notes: The microassembler converts the microcode into actual signal values
The sequencing field is used along with the opcode to determine the next state

## Slide 32: Multi-Cycle Performance
Example 1. Compare the performance of the multi-cycle and single-cycle implementations for the SPECINT2000 program which has the following instruction mix: 25% loads, 10% stores, 11% branches, 2% jumps, 52% ALU.
TimeSC = IC x CPISC x CCSC
= IC x 1 x CCSC = ICSC x CCSC
TimeMC = IC x CPIMC x CCMC
CPIMC = 0.25x5 + 0.1x4 + 0.11x3 + 0.02 x 3 + 0.52 x 4 = 4.12
CCMC = 1/5 * CCSC (Is that true!!)
Speedup = TimeSC / TimeMC = 5 / 4.12 = 1.21 !
Multi-cycle is cost effective as well, as long as the time for different processing units are balanced!

## Slide 33: Multi-Cycle Performance
Single-Cycle
Multi-Cycle
This is true as long as the delay of all functional units is balanced!
LW
SW
Cycle 1
Cycle 2
waste
LW
SW
Instr

## Slide 34: Multi-Cycle Performance
Example 2. Redo example 1 without assuming that the cycle time for multi-cycle is 1/5 that of single cycle. Assume the delay times of different units as given in the table.
TimeSC = IC x CPISC x CCSC
= IC x 1 x 600 = 600 IC
TimeMC = IC x CPIMC x CCMC
CPIMC = 0.25x5 + 0.1x4 + 0.11x3 + 0.02 x 3 + 0.52 x 4 = 4.12
CCMC = 200 (should match the time of the slowest functional unit)
TimeMC = IC x 4.12x 200 = 824 IC
Speedup = TimeSC / TimeMC = 600 / 824= 0.782 !
Unit | Time (ps)
Memory | 200
ALU and adders | 100
Register File | 50